## Slide 1: Design of a Fuzzy-PID Controller for Controlling Quadrotor Attitude and Altitude
Prepared by,
Mrinmoy Sarkar & Brian Baity
Advisor,
Dr. Abdollah homaifar

## Slide 2: Overview
Motivation
Challenges
Mathematical modeling of quadrotor
PID controller design
Fuzzy-PID controller design
Simulation
Conclusion

## Slide 3: Motivation
Fuzzy PID Controller solves the problem of fixed gain
Fuzzy PID Controller is cheaper to develop
Fuzzy PID Controller covers a wider range of operating conditions
Fuzzy PID Controllers are more readily customizable
Fuzzy PID Controller is robust in terms of uncertainty

## Slide 4: Challenges
Nonlinear system
Under actuated system
Low on board processing capability
Low operation time
Low efficiency in power consumption

## Slide 5: Mathematical modeling of quadrotor
Structure of a quadrotor
He, Z. and Zhao, L., 2014. A simple attitude control of quadrotor helicopter based on ziegler-nichols rules for tuning pd parameters. The Scientific World Journal, 2014.

## Slide 6: Cont.
He, Z. and Zhao, L., 2014. A simple attitude control of quadrotor helicopter based on ziegler-nichols rules for tuning pd parameters. The Scientific World Journal, 2014.

## Slide 7: Cont.
He, Z. and Zhao, L., 2014. A simple attitude control of quadrotor helicopter based on ziegler-nichols rules for tuning pd parameters. The Scientific World Journal, 2014.

## Slide 8: Cont.
Dynamic Model: The dynamics model is composed of the rotational and translational motions. The rotational motion is fully actuated, while the translational motion is underactuated. In the body coordinate system, the rotational motion equations are derived according to the law of momentum theorem and gyroscopic effect of quadrotor, and they are given by,
He, Z. and Zhao, L., 2014. A simple attitude control of quadrotor helicopter based on ziegler-nichols rules for tuning pd parameters. The Scientific World Journal, 2014.

## Slide 9: Cont.
The Motion Equations of Quadrotor:
He, Z. and Zhao, L., 2014. A simple attitude control of quadrotor helicopter based on ziegler-nichols rules for tuning pd parameters. The Scientific World Journal, 2014.

## Slide 10: Cont. (State space model)
He, Z. and Zhao, L., 2014. A simple attitude control of quadrotor helicopter based on ziegler-nichols rules for tuning pd parameters. The Scientific World Journal, 2014.

## Slide 11: Underactuation
Underactuation is a technical term used in robotics and control theory to describe mechanical systems that cannot be commanded to follow arbitrary trajectories in configuration space. This condition can occur for a number of reasons, the simplest of which is when the system has a lower number of actuators than degrees of freedom. In this case, the system is said to be trivially underactuated.
The class of underactuated mechanical systems is very rich and includes such diverse members as automobiles, airplanes, and even animals.

## Slide 12: PID Controller Design
Quadrotor control structure
He, Z. and Zhao, L., 2014. A simple attitude control of quadrotor helicopter based on ziegler-nichols rules for tuning pd parameters. The Scientific World Journal, 2014.

## Slide 13: Hovering Condition
For hovering,
Φ = 0;
θ = 0;
Ψ = 0;
Φ`` = 0;
Θ`` = 0;
Ψ`` = 0;
X`` = 0;
Y`` = 0;
Z`` = 0;
So, for hovering Condition the control inputs are,
U1 = mg
U2 = (1/b1)(-a1θ`Ψ` + a2θ`Ωr)
U3 = (1/b2)(-a3Φ`Ψ` - a4Φ`Ωr)
U4 = (1/b3)(-a5θ`Φ`)
He, Z. and Zhao, L., 2014. A simple attitude control of quadrotor helicopter based on ziegler-nichols rules for tuning pd parameters. The Scientific World Journal, 2014.

## Slide 14: Feedback Linearization
He, Z. and Zhao, L., 2014. A simple attitude control of quadrotor helicopter based on ziegler-nichols rules for tuning pd parameters. The Scientific World Journal, 2014.

## Slide 15: Laplace Transformation of the Linear Model and PID Controller
He, Z. and Zhao, L., 2014. A simple attitude control of quadrotor helicopter based on ziegler-nichols rules for tuning pd parameters. The Scientific World Journal, 2014.
Where,
kp = proportional gain
ki = integral gain
kd = differential gain

## Slide 16: Altitude Controller
Heba talla Mohamed Nabil ElKholy, 2014. Dynamic Modeling and Control of a Quadrotor Using Linear and
Nonlinear Approaches, Thesis for degree of Master of Science in Robotics, Control and Smart Systems, 2014.
Block Diagram for Altitude Controller

## Slide 17: Attitude and Heading Controller
Block Diagram for Attitude and Heading Controller
Heba talla Mohamed Nabil ElKholy, 2014. Dynamic Modeling and Control of a Quadrotor Using Linear and
Nonlinear Approaches, Thesis for degree of Master of Science in Robotics, Control and Smart Systems, 2014.

## Slide 18: Position Controller
Position can not be controlled directly for a quadcopter.
Heba talla Mohamed Nabil ElKholy, 2014. Dynamic Modeling and Control of a Quadrotor Using Linear and
Nonlinear Approaches, Thesis for degree of Master of Science in Robotics, Control and Smart Systems, 2014.

## Slide 19: Position Controller (cont.)
Heba talla Mohamed Nabil ElKholy, 2014. Dynamic Modeling and Control of a Quadrotor Using Linear and
Nonlinear Approaches, Thesis for degree of Master of Science in Robotics, Control and Smart Systems, 2014.
Block Diagram for Position Controller

## Slide 20: Simulation
Parameters | Description | Values
m | Quadrotor mass | 0.4794 kg
g | Gravitational acceleration | 9.8 m/s2
l | Moment arm | 0.225 m
Ix | MOI about body frame's x-axis | 0.0086 kg.m2
Iy | MOI about body frame's y-axis | 0.0086 kg.m2
Iz | MOI about body frame's z-axis | 0.0172 kg.m2
Jr | Rotor inertia | 3.7404 x 10-5 kg.m2
b | Aerodynamic force constant | 3.13 x 10-5 N.s2
d | Aerodynamic moment constant | 9 x 10-7 Nm.s2
K2 | Linearization constant | -14.6211
K3 | Linearization constant | -14.6211
K4 | Linearization constant | -32
He, Z. and Zhao, L., 2014. A simple attitude control of quadrotor helicopter based on ziegler-nichols rules for tuning pd parameters. The Scientific World Journal, 2014.

## Slide 21: Simulink Model

## Slide 22: Altitude Controller(Simulation Result)
Parameter | Description | Value
kp | Proportional gain | 30
ki | Integral gain | 0
kd | Derivative gain | 10
tr | Rising time | 702.5 ms
ts | Settling time | 1.5 s
%OS | Overshoot | 0

## Slide 23: Roll Controller
Parameter | Description | Value
kp | Proportional gain | 2.9996
ki | Integral gain | 0.17
kd | Derivative gain | 0.87
tr | Rising time | 110.1 ms
ts | Settling time | 597.5 ms
%OS | Overshoot | 1.37

## Slide 24: Pitch Controller
Parameter | Description | Value
kp | Proportional gain | 2.9996
ki | Integral gain | 0.17
kd | Derivative gain | 0.87
tr | Rising time | 110.1 ms
ts | Settling time | 597.5 ms
%OS | Overshoot | 1.37

## Slide 25: Yaw Controller
Parameter | Description | Value
kp | Proportional gain | 3.9
ki | Integral gain | 0
kd | Derivative gain | 2.57
tr | Rising time | 94 ms
ts | Settling time | 1.5s
%OS | Overshoot | 6.09

## Slide 26: Position Controller (X)
Parameter | Description | Value
kp | Proportional gain | 19.5
ki | Integral gain | 0
kd | Derivative gain | 5.7
tr | Rising time | 592.8 ms
ts | Settling time | 1.83 s
%OS | Overshoot | 8.42

## Slide 27: Position Controller (Y)
Parameter | Description | Value
kp | Proportional gain | 19.5
ki | Integral gain | 0
kd | Derivative gain | 5.7
tr | Rising time | 592.8 ms
ts | Settling time | 1.83 s
%OS | Overshoot | 8.42

## Slide 28: Simulation of Quadrotor on a Circular Trajectory
Plot of the Trajectory in 2d
Plot of the Trajectory in 3d

## Slide 29: Simulation of Quadrotor on a Circular Trajectory

## Slide 30: Tuning of Conventional PID Controller

## Slide 31: Principle of Fuzzy Logic Controller (FLC)
FLC implementations require the following:
1) Fuzzification
2) Knowledge Base
a. Data Base
b. Rule Base
3) Fuzzy inference system
4) Defuzzifcation

## Slide 32: Design and Tuning Sample

## Slide 33: To be Continued …